## Slide 1
Inspection
Contract
RFQ/RFP
Gas Utility
Service Provider
&
Gas Utility
Inspection Provider
Personnel Needs
Review
Equipment Needs
Review
Project Startup
Train - Mobilize
Job Costing
Report to
Accounting
Accounts
Payable
Management
Personnel
Traffic Control
Permits
Sewer Utility &
Gas Utility
Inspect
Sewer Main
Lateral
Inspection
Possible from
Main?
Locate Cleanout
Or House Access
To Lateral
Document / Notify
Lack of Access
In Final Report
Request Property
Access -
Call or Letter
Collect Lateral
Inspection Data
From Sewer Main
Collect Lateral
Inspection Data
From
Cleanout/House
Access Provided
w/ Possible Utility
Assistance
Document / Notify
Lack of Access
In Final Report
Gas Cross Bore
Found
Document / Notify
Cross Bore Found
Fix Cross Bore,
Report /
Reinspect/Verify
No
Yes
Transfer Inspection
Info To QA/QC -
Data Center
QA/QC
Check for Image
Quality, Accuracy,
Completeness,
GPS Logs,
Run Batches/Stats.
Updated GIS
Gas Cross Bore
Found
Reconcile Problem
Document / Notify
in Final Report
& Project Data
Deliver Final Report
To Gas Line Utility
Accounts
Receivable
CCTV
Sewer Main,
Ext. Cleanout
Or House
Optional
To Final Report
Provide Gas
Mapping & Data
Legacy Cross Bore Inspection Process Chart (Basic) - Gas Distribution
Gas Line Utility
Review & Approval
of Final Report
Invoice Gas
Line Client
Other Utility
Cross Bore
Found
Direction
Other Utility
Cross Bore
Found
Determine
System’s Cross
Bore Risk
Legend
Review Data -
Determine Inspect.
Method (Scope)
Document
Cross Bore
Fix
Report
to Utility
Management
Collect Data &
Model Risk
Process
Development /
Approval
Sewer Access
Agmt. / Permits
Municipality
Property Owner /
Occupant
© Copyright 2020. Cross Bore Safety Association. All Rights Reserved. www.crossboresafety.org